EGR 270

Fundamentals of Computer Engineering

File:  Pinouts

Lab Reference Sheets

This document contains useful information for constructing and testing digital logic circuits, including:

- Pinouts

- Data sheets

- Capacitor markings and values available in lab

- Standard 5% and 10% Resistor and the resistor color code

- SK-10 breadboard and an example circuits wired on the breadboard

- Building a 5V power supply using a 9V battery and a 5V regulator

This document is available from the instructor’s web page in both Adobe Acrobat format and in Microsoft Word format.  If you download the Microsoft Word file, you can copy any of the pinout or other information that you wish into lab reports or other locations.

The Drawing Tools in Microsoft Word were used to create the pinouts and circuits.  The Drawing Tools menu usually appears at the bottom of the screen in Word.  If it does not, pick View - Toolbars - Drawing from the menu.  Each pinout has been grouped so that it can be easily moved and resized.  To edit a pinout, select the object and then pick Draw - Ungroup from the Drawing Tools menu.

Data Sheets

Data sheets for the devices listed below, along with a number of other devices, are available on the instructor’s web page.

- 7400 – Quad 2-input NAND

- 74HC00 – CMOS Quad 2-input NAND

- 7401 – Open-collector Quad 2-input NAND

- 7406/7416 – Open-collector inverter

- 7447A – BCD-to-7-segment-decoder/driver (for common anode displays)

- 7476– JK flip-flop with Preset and Clear

- 74151 – 8x1 multiplexer (data selector)

- 74155/74156 – Dual 2x4 decoder

- 74191 – Synchronous 4-Bit Up/Down Counter

- 555 – Timer

- GAL22V10 – Programmable Logic Device (PLD)

Page 2

Page 3

Page 4

Page 5

Page 7

Page 8

## Page 9

Capacitor values available in the EGR 270 lab

(all values are in (F)

| .001 | .01 | .1 | 1 | 10 | 100 | 1000 |
| --- | --- | --- | --- | --- | --- | --- |
|  | .015 | .15 |  | 12, 15 | 120 | 1500 |
| .0022 | .022 | .22 | 2.2 | 22 | 200, 220 |  |
|  | .027 | .27 | 3 | 25 |  |  |
| .0033 | .033 | .33 | 3.3 | 33 |  |  |
| .0047 | .047 | .47 | 4.7 | 47 | 470 |  |
|  |  | .56 | 5 | 50 | 500 |  |
| .0068 | .068 | .68 | 6.8 |  |  |  |
|  | .082 | .82 |  |  |  |  |

Polarized capacitors:

Polarity is important on some capacitors.  Most capacitors that look like metal cans are electrolytic capacitors and are polarized.  If a capacitor is polarized it should have a terminal marked as being positive (+) or negative (-).  Be sure to connect it with the proper polarity.  Connecting a polarized capacitor with reverse polarity can sometimes yield errors and in extreme cases the capacitors can explode!  Some common markings for polarized capacitors are shown below.

Capacitors values:

Capacitors vary tremendously in size, color, shape, and material.  The markings on capacitors also vary considerably and they can often be difficult to interpret since various styles are used to specify the value of capacitance.  It is a good idea to check capacitor values in lab using an impedance bridge if one is available.  Several examples of labels found on capacitors are shown below.

Page 10

# Standard values of commercially available resistors

| Ohms (() | Kilohms (k() | Megohms (M() |
| --- | --- | --- |
| 0.10 | 1.0 | 10 | 100 | 1000 | 10 | 100 | 1.0 | 10.0 |
| 0.11 | 1.1 | 11 | 110 | 1100 | 11 | 110 | 1.1 | 11.0 |
| 0.12 | 1.2 | 12 | 120 | 1200 | 12 | 120 | 1.2 | 12.0 |
| 0.13 | 1.3 | 13 | 130 | 1300 | 13 | 130 | 1.3 | 13.0 |
| 0.15 | 1.5 | 15 | 150 | 1500 | 15 | 150 | 1.5 | 15.0 |
| 0.16 | 1.6 | 16 | 160 | 1600 | 16 | 160 | 1.6 | 16.0 |
| 0.18 | 1.8 | 18 | 180 | 1800 | 18 | 180 | 1.8 | 18.0 |
| 0.20 | 2.0 | 20 | 200 | 2000 | 20 | 200 | 2.0 | 20.0 |
| 0.22 | 2.2 | 22 | 220 | 2200 | 22 | 220 | 2.2 | 22.0 |
| 0.24 | 2.4 | 24 | 240 | 2400 | 24 | 240 | 2.4 |  |
| 0.27 | 2.7 | 27 | 270 | 2700 | 27 | 270 | 2.7 |  |
| 0.30 | 3.0 | 30 | 300 | 3000 | 30 | 300 | 3.0 |  |
| 0.33 | 3.3 | 33 | 330 | 3300 | 33 | 330 | 3.3 |  |
| 0.36 | 3.6 | 36 | 360 | 3600 | 36 | 360 | 3.6 |  |
| 0.39 | 3.9 | 39 | 390 | 3900 | 39 | 390 | 3.9 |  |
| 0.43 | 4.3 | 43 | 430 | 4300 | 43 | 430 | 4.3 |  |
| 0.47 | 4.7 | 47 | 470 | 4700 | 47 | 470 | 4.7 |  |
| 0.51 | 5.1 | 51 | 510 | 5100 | 51 | 510 | 5.1 |  |
| 0.56 | 5.6 | 56 | 560 | 5600 | 56 | 560 | 5.6 |  |
| 0.62 | 6.2 | 62 | 620 | 6200 | 62 | 620 | 6.2 |  |
| 0.68 | 6.8 | 68 | 680 | 6800 | 68 | 680 | 6.8 |  |
| 0.75 | 7.5 | 75 | 750 | 7500 | 75 | 750 | 7.5 |  |
| 0.82 | 8.2 | 82 | 820 | 8200 | 82 | 820 | 8.2 |  |
| 0.91 | 9.1 | 91 | 910 | 9100 | 91 | 910 | 9.1 |  |

Notes:  	All values are available with 5% tolerance.

Only the bold values are available with 10% tolerance.

# Resistor Color Code

Carbon resistors are typically color-coded using four colored bands labeled A, B, C, and D as indicated below.

| Bands A, B, C | Band D |
| --- | --- |
| Black | 0 | Gold | 5% |
| Brown | 1 | Silver | 10% |
| Red | 2 | No band | 20% |
| Orange | 3 |  |  |
| Yellow | 4 |  |  |
| Green | 5 |  |  |
| Blue | 6 |  |  |
| Violet | 7 |  |  |
| Gray | 8 |  |  |
| White | 9 |  |  |
| Gold | -1 |  |  |
| Silver | -2 |  |  |

The size of a carbon resistor indicates its power rating.

Page 11

SK-10 Solderless Breadboard (or equivalent)

# Internal Connections on the SK-10 Solderless Breadboard

## Notes:  	1)  Lines indicate which holes are connected under the breadboard.

2)  To connect two or more wires together, plug them in the same row of holes.

3)  Holes A and B are connected on some breadboards (as well as the similar holes on the other horizontal rows).

Page 12

Example:  Connect the following circuit using the SK-10 solderless breadboard.

## Page 13

Example:  Connect the following circuit using the SK-10 solderless breadboard.

Notes:

- The DIP switch operates as follows:

ON  – Provides a logical 0 (LOW).  Closed switch makes connection to ground.

OFF – Provides a logical 1 (HIGH).  Open switch provides 5V through the 2.2k resistor.

(It is often useful to install the switch upside down so that ON (LOW) is on the bottom.)

- The switch positions shown above (darkened) provide an input of 110 causing the red LED to light indicating that the output is logical 1 (HIGH).

- Cutting wires to length and using a wire color scheme makes for a neat circuit that is easy to troubleshoot.  In the circuit above the following color scheme was used:

RED – 5V

BLACK – Ground (0V)

GREEN – Switch connections

### BLUE – Other connections

# Text boxes

Gnd

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

7401

13

Gnd

Gnd

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

7402

13

Gnd

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

Gnd

7400

13

7402 Quad 2-input NOR

7401 Quad 2-input NAND

(open-collector outputs)

7400 Quad 2-input NAND

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

7408

13

Gnd

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

7405, 7406, 7416

13

Gnd

7411 Triple 3-input AND

7410 Triple 3-input NAND

7408 Quad 2-input AND

7405, 7406, 7416 Hex Inverter

(open-collector outputs)

7404 Hex Inverter

7

6

5

4

3

8

9

10

11

12

14

Vcc

7420

13

2

1

NC

NC

Gnd

7

6

5

4

3

8

9

10

11

12

14

Vcc

Gnd

7411

13

2

1

7

6

5

4

3

8

9

10

11

12

14

Vcc

Gnd

7410

13

2

1

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

7404

13

Gnd

7420 Dual 4-input NAND

7432 Quad 2-input OR

7427 Triple 3-input NOR

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

Gnd

7486

13

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

Gnd

7432

13

7

6

5

4

3

8

9

10

11

12

14

Vcc

Gnd

7427

13

2

1

7486 Quad 2-input Exclusive-OR

7

6

5

4

3

2

1

10

11

12

13

14

16

Vcc

7447A

15

8

9

Gnd

B

C

LT

BI/RBO

RBI

D

A

e

f

g

a

b

c

d

7447A   BCD to 7-segment decoder/driver:  Pinout and Logic Symbol

7

6

5

4

3

2

1

10

11

12

13

14

16

Vcc

7476

15

8

9

Gnd

Q

Q

2J

K

J

CLR

PR

CK

Q

Q

PR

CLR

CK

J

K

1CK

2CLR

2Q

2Q

2K

1Q

1Q

1K

2PR

2CK

1J

1CLR

1PR

7476  Dual JK Flip-Flop:  Pinout and Logic Symbols

7

6

5

4

3

2

1

10

11

12

13

14

16

Vcc

15

8

9

C0

1

A4

A2

A1

B1

Gnd

C4

4

B4

B2

2

B3

A3

3

4

C4

C0

B1

A1

1

A4

B4

3

A3

B3

2

B2

A2

7483A

7485   4-Bit Magnitude Comparator:  Pinout and Logic Symbol

7

6

5

4

3

2

1

10

11

12

13

14

16

A>B

out

15

8

9

A2

B0

B3

Gnd

A0

B1

A1

B2

A3

Vcc

A<B

out

A=B

out

A>B

in

A=B

in

A<B

in

A3

B2

A2

B1

A0

B0

B3

A1

A<B

in

7485

A=B

in

A>B

in

A>B

out

A=B

out

A<B

out

7483A   4-Bit Adder:  Pinout and Logic Symbol

7

6

5

4

3

2

1

10

11

12

13

14

16

Z

15

8

9

I6

S2

I3

Gnd

S1

S0

I7

I5

I4

Vcc

E

Z

I0

I1

I2

I4

I5

I6

S0

S1

S2

I3

I7

I2

74151

I1

I0

Z

Z

E

74151   8x1 Data Selector/Multiplexer:  Pinout and Logic Symbol

7

6

5

4

3

2

1

8

9

10

11

12

14

Input

D

13

QC

Serial

Input

CLK2

CLK1

QD

QB

QA

Vcc

Gnd

Mode

Input

C

Input

B

Input

A

QA

QD

QB

QC

CLK2

Serial

Input

InA

InB

7495A

InC

InD

Mode

CLK1

7495A   4-Bit Parallel-Load Shift Register:  Pinout and Logic Symbol

7493A   4-Bit Binary Counter:  Pinout and Logic Symbol

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

13

QD

CKB

QC

QB

Gnd

QA

NC

CKA

NC

NC

NC

R02

R01

QA

QD

QB

QC

B

A

R01

R02

7493A

7490A   Decade Counter:  Pinout and Logic Symbol

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

13

QD

CKB

QC

QB

Gnd

QA

NC

CKA

R92

R91

NC

R02

R01

QA

QD

QB

QC

B

A

R01

R02

R91

R92

7490A

1Y2

7

6

5

4

3

2

1

10

11

12

13

14

16

15

8

9

A

2Y0

1C

Gnd

2Y1

2Y2

2Y3

2G

2C

Vcc

1Y0

1Y1

1Y3

B

1G

2C

2G

A

2Y2

2Y1

2Y0

1C

2Y3

1G

74155/74156

B

1Y3

1Y2

1Y1

1Y0

7

6

5

4

3

2

1

18

19

20

21

22

24

Input

23

8

17

Input/

Clock

Input

Input/

Output

Vcc

Input

Input

Input

Input

Input

GAL22V10

11

10

9

14

15

16

Input

12

13

Gnd

Input

Input

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input/

Output

Input

GAL22V10  PLD (Programmable Logic Device)

7

6

5

4

3

2

1

10

11

12

13

14

16

UP

15

8

9

BO

D

B

Gnd

C

LOAD

CO

CLR

A

Vcc

QD

QC

DOWN

QA

QB

A

CLR

BO

LOAD

C

D

B

CO

QB

74192/74193

QA

DOWN

UP

QC

QD

74192 – BCD Counter

74193 – 4-Bit Binary Counter

74192/74193   Synchronous Up/Down Counter:  Pinout and Logic Symbol

7

6

5

4

3

2

1

10

11

12

13

14

16

D/U

15

8

9

RCO

D

B

Gnd

C

LOAD

MAX/

MIN

CLK

A

Vcc

QD

QC

CTEN

QA

QB

A

CLK

RCO

LOAD

C

D

B

MAX/

MIN

QB

74190/74191

QA

CTEN

D/U

QC

QD

74190 – BCD Counter

74191 – 4-Bit Binary Counter

74190/74191   Synchronous Up/Down Counter:  Pinout and Logic Symbol

74155 – Totem Pole Outputs

74156 – Open-Collector Outputs

74155/74156   Dual 2-Line To 4-Line Decoder/Demultiplexer:  Pinout and Logic Symbol

Page 6

5

6

8

Vcc

7

Control

Voltage

Threshold

Discharge

1

2

3

4

Gnd

Trigger

Output

Reset

555

Example:  If C = 0.1 (F, RA = 5 k(, and

RB = 4.4 k(,

then TH = 651.4 (s, TL = 304.9 (s,

T = 956.3 (s,  f = 1046 Hz, and D = 68.1 %

H

T

T

L

T

Time

Output

Voltage

Vcc

0

5

6

8

Vcc

7

Control

Voltage

Threshold

Discharge

1

2

3

4

Gnd

Trigger

Output

Reset

555

T = 1.1RC

Time

Output

Voltage

Vcc

Falling edge of trigger

voltage fires the one-shot

Time

Trigger

Voltage

Vcc

Trigger should return

to Vcc

Example:  If C = 0.1 (F and R = 47 k(, then T = 1.1(47 k()(0.1 (F) = 5.17 ms.

So, each time the one-shot is triggered, an output pulse with a duration of 5.17 ms is produced.

B

E

C

7805

B     C     E

7

6

5

4

3

2

1

8

9

10

11

12

14

Vcc

LM339

13

+

_

+

_

+

_

+

_

Out2

Out1

Out3

Out4

In4+

Gnd

In4-

In3+

In3-

In2+

In2-

In1+

In1-

TIP30  PNP Transistor Symbol and Pin Assignment

LM339 Quad Comparator

(open-collector outputs)

7805

6 – 35V  in

5V  out

+

_

_

+

7805 5V Regulator

Vin

Vout

+

_

_

+

3 (ADJ)

1

Vin

2

Vout

5k

240

C1

0.F

C2

1F

LM317T Adjustable  Regulator

Notes:

1)  C1 is optional – improves transient response

2)  C2 is needed only if device is far from filter capacitors

3)  Vout adjustable +1.2V to +37V

4)  Vout is tied to the heat sink

LM317T

3

ADJ

2

Vout

1

Vin

7

6

4

2

1

8

9

12

14

d

13

b

c

a

DP

g

f

e

No

Pin

Common

Cathode

No

Pin

No

Pin

No

Pin

Common

Cathode

7

6

3

2

1

8

9

10

11

14

Common

Anode

e

13

b

d

g

NC

c

f

a

DP

No

Pin

Common

Anode

No

Pin

No

Pin

Common Cathode 7-segment Display

(common cathode connection to ground)

Common Anode 7-segment Display

(common anode connection to Vcc)

4

5

2

1

3

6

7

8

9

10

a

c

NC

dp

f

d

g

Common

Anode

b

e

GNS-3011 Common Anode 7-segment Display

(common anode connection to Vcc)

"Hold it!  I said 2 MICRO farads!"

+

+

+

The longer lead is generally positive

+

+

+

_

_

_

_

+

47/25

M

.001K

1000

100J

C = 47 (F

35V rating

+ terminal marked

104

C = 0.1 (F

(Note that 104 = 10 x 104 pF

= 10510-12F = 10-7F

= 0.1 x 10-6 F =  0.1 (F)

+(47+35V

C = 100 pF

(Note that MMFD = ((F

= 10-610-6F = 10-12F = pF)

100 MMFD

C = 10 (F

10 MFD

C = 3 (F

3 UF

C = 0.001 (F

1000V rating

K = 10% tolerance

C = 47 (F

25V rating

M = 20% tolerance

C = 100 pF

J = 5% tolerance

A

B

C

D

A – First significant digit

B – Second significant digit

C – Exponent

D – Tolerance

Resistance value:  R = AB x 10C

Ex:  Green, Blue, Red, Silver

R = 56 x 102 = 5.6 k(, 10% tolerance

¼ W

½ W

1 W

2 W

A         B

+

_

2.2 k

5.6 k

3.3 k

1.0 k

1.5 k

10 V

Jumper

Jumper

+

_

Connections to

10 V power supply

Switch_A

LED

Switch_B

Switch_C

U1

U2

13

12

11

13

12

11

ON

OFF

Jumper

Jumper

7408

7432

A B C

7805

6 – 35V  in

5V  out

+

_

_

7805 5V Regulator

+

9V Battery

+

_

A741  Operational Amplifier:  Pinout and Symbol

5

6

8

Gnd

7

Offset2

Output

-VDC

1

2

3

4

Offset1

Inverting

Input

Non-Inverting

Input

+VDC

A741