SK-10 Solderless Breadboard (or equivalent)

# Internal Connections on the SK-10 Solderless Breadboard

## Notes:  	1)  Lines indicate which holes are connected under the breadboard.

2)  To connect two or more wires together, plug them in the same row of holes.

3)  Holes A and B are connected on some breadboards (as well as the similar holes on the other horizontal rows).

Example:  Connect the following circuit using the SK-10 solderless breadboard.

Example:  Connect the following circuit using the SK-10 solderless breadboard.

Notes:

- The DIP switch operates as follows:

ON  – Provides a logical 0 (LOW).  Closed switch makes connection to ground.

OFF – Provides a logical 1 (HIGH).  Open switch provides 5V through the 2.2k resistor.

(It is often useful to install the switch upside down so that ON (LOW) is on the bottom.)

- The switch positions shown above (darkened) provide an input of 110 causing the red LED to light indicating that the output is logical 1 (HIGH).

- Cutting wires to length and using a wire color scheme makes for a neat circuit that is easy to troubleshoot.  In the circuit above the following color scheme was used:

RED – 5V

BLACK – Ground (0V)

GREEN – Switch connections

### BLUE – Other connections

# Text boxes

A         B

Jumper

Jumper

+

_

Connections to

10 V power supply

+

_

2.2 k

5.6 k

3.3 k

1.0 k

1.5 k

10 V

11

12

13

11

12

13

U2

U1

Switch_C

Switch_B

LED

Switch_A

ON

OFF

7805 5V Regulator

Jumper

Jumper

7408

7432

A B C

+

_

_

+

5V  out

6 – 35V  in

7805

9V Battery

+

_