## Slide 1
Reading Assignment: Chapter 6 in Electric Circuits, 9th Ed. by Nilsson
Demonstration: Pass around various types of capacitors in class.
Chapter 6 – Capacitors and Inductors
Two new passive components are introduced in this chapter. They are both considered to be energy-storage devices:
Capacitor – stores energy in an electric field
Inductor – stores energy in a magnetic field
1
Chapter 6 EGR 271 – Circuit Theory I
Capacitor symbol

## Slide 2
Capacitors
The simplest type of capacitor is a parallel plate capacitor. Consider the result of placing a voltage across two parallel plates as shown below.
+
_
+ + + + + +
+ + + + + + + +
+ + + + + + + +
_ _ _ _ _ _ _
_ _ _ _ _ _ _ _ _ _ _ _ _ _
Electrons are attracted to the positive terminal of the source leaving a depletion of electrons and a positively charged plate.
Charge = +Q
Electrons are repelled by the negative terminal of the source leaving an abundance of electrons and a negatively charged plate.
Charge = -Q
-
-
-
-
-
-
Total Charge = (+Q) + (-Q) = 0
2
Chapter 6 EGR 271 – Circuit Theory I

## Slide 3
Charge and capacitance
The charge on each plate is proportional to the voltage across the plates, so
Q  V or more specifically
Q = CV
where C = capacitance
Typical values: The Farad is a large unit. Most capacitors have capacitance values in the F, nF, or pF range; although some capacitors in the F range are available (generally at low voltages).
Electric field
As discussed in Chapter 1, a force is exerted between oppositely charged particles (it can be calculated using Coulomb’s Law). When charged is distributed over a surface (such as with the plates of a capacitor), this force is represented by an electric field, E. The electric field is measured as force per unit charge, or E = F/Q. The electric field is represented by electric flux lines. Recall that a capacitor is an energy storage device – it stores energy in an electric field. Electric fields are studied in depth in a course in electromagnetism.
+ + + + + + + + + +
- - - - - - - - - -
E
Electric flux lines
An electric field, E, exists between the charged plates of a capacitor
3
Chapter 6 EGR 271 – Circuit Theory I

## Slide 4
Capacitance symbol
The capacitor is a passive device so the relationship above depends on the use of passive sign convention. The general symbol for a capacitor is shown below. Note that the symbol looks like two parallel plates.
Capacitor current
Recall that current for any device can be found using the relationship:
so capacitor current is found as follows:
Key relationship: This is sort of like Ohm’s Law for a capacitor.
4
Chapter 6 EGR 271 – Circuit Theory I

## Slide 5
Physical Characteristics
Capacitance can also be determined from the physical dimensions of the capacitor using
A = Area of plate (in m2)
d = distance between plates (in m)
d
Dielectric = material between the plates
and
 = permittivity of the dielectric (in F/m)
where  , A, and d
are illustrated in
the figures shown.
5
Chapter 6 EGR 271 – Circuit Theory I

## Slide 6
The permittivity of a given material is often expressed in terms of how it relates to the permittivity of a vacuum using:
 = R o
where o = permittivity of a vacuum = 8.85 x 10-12 F/m
R = relative permittivity (a few examples are shown below)
Dielectric strength is a measure of how much voltage would be required to jump across a gap, similar to how a spark jumps across the gap on a spark plug. Note that if a spark plug uses a gap of 0.032”, a voltage of = (32 mil)(75V/mil) = 2400V is necessary to create a spark.
A dielectric for a capacitor is chosen to insure that the voltage will not arc across the capacitor. So the voltage rating for a capacitor is related to the dielectric strength and the gap size (which affects the value of C).
Note: 1 mil = 0.001”
6
Chapter 6 EGR 271 – Circuit Theory I

## Slide 7
Example: Calculate the value of C for a teflon capacitor with rectangular plates that measure 2 cm by 4 cm, and a distance of 0.1 mm between the plates. Also calculate the maximum voltage rating for the capacitor.
7
Chapter 6 EGR 271 – Circuit Theory I

## Slide 8
Variable Capacitors
Recall that
so how can C be varied?
1) by varying d, the distance between the plates
2) by varying A, the area between the plates
(actually by rotating one plate to change
the amount of overlap between plates).
Method 1: Varying d
Tightening the screw reduces
the distance between the plates
and increases C.
Method 2: Varying A
Turning the screw changes the amount of overlap between the plates.
No overlap
100% overlap
50% overlap
Bottom view
Top view
Note: Using multiple plates acts like capacitors in parallel which add together (to be proven shortly)
Reference: All Electonics (www.allelectronics.com
Reference: Intro. Circuit Theory I, 6th Ed., by Boylestad
8
Chapter 6 EGR 271 – Circuit Theory I

## Slide 9
Two categories of capacitors
Capacitors are sometimes separated into two categories:
1) Polarized (electrolytic)
2) Non-polarized (non-electrolytic)
Electrolytic capacitors
have polarity markings and may be damaged (or even explode) if used with reverse polarity
are often cylindrical shaped (appear like a metal can)
are constructed using a large roll of aluminum foil coated with Al·O2 where the aluminum acts as the positive plate and the oxide as the dielectric. A layer of paper is placed over oxide coating and then another roll of aluminum foil without the oxide coating is added to act as the negative plate. This results in a very large plate area, A, and a very small distance, d, between the plates (the thickness of the oxide coating).
most large capacitors (F range) are electrolytic
Non-electrolytic capacitors
Most small capacitors (nF and pF range) are non-electrolytic
9
Chapter 6 EGR 271 – Circuit Theory I

## Slide 10
Capacitor symbols - A special symbol is often used with electrolytic capacitors to designate the negative terminal as shown below.
Image 3: Tomographic image of the capacitor showing the roll of foil inside.ctrolytic capacitor showing the roll of aluminum foil (reference: Oak Ridge National Labs (www.ornl.com)
Image 1: External view of an electrolytic capacitor
Image 2: Digital radiograph of the capacitor showing the roll of foil inside.
Electrolytic capacitors - images showing internal construction
Reference: Oak Ridge National Labs (www.ornl.com)
10
Chapter 6 EGR 271 – Circuit Theory I

## Slide 11
Various types of capacitors (reference: All Electronics (www.allelectronics.com)
Ceramic Disc
Capacitor
(0.22F, 1000V)
Mylar Capacitor (0.22F, 100V)
Axial Electrolytic Capacitor (47F, 25V)
DIP Capacitor (2.2nF, 50V)
Monolithic Ceramic Capacitor (22nF)
Snap In Capacitor (330F, 400V)
Super Capacitor (1F, 2.5V)
Photo Flash Capacitor (150F, 300V)
Radial Electrolytic Capacitor (47F, 25V)
Metalized Polyester
Capacitor
(2F, 200V)
11
Chapter 6 EGR 271 – Circuit Theory I

## Slide 12
Key capacitor relationships:
Show that
12
Chapter 6 EGR 271 – Circuit Theory I

## Slide 13
Example: Find i(t) through the capacitor shown if v(t) = 6e-2t V.
Example: Calculate the maximum energy that could be stored in two of the capacitors that were passed around in class.
Example: Find v(t) across the capacitor shown if i(t) = 10cos(400t) mA.
13
Chapter 6 EGR 271 – Circuit Theory I

## Slide 14
Example: Sketch i(t), p(t), and w(t) if the graph of v(t) shown below represents the voltage across a 100 F capacitor.
14
Chapter 6 EGR 271 – Circuit Theory I

## Slide 15
Series Capacitance
Use KVL to show that
(Series capacitors combine like parallel resistors)
15
Chapter 6 EGR 271 – Circuit Theory I

## Slide 16
Parallel Capacitance
Use KCL to show that
(Parallel capacitors combine like series resistors)
Example: Find the equivalent capacitance between terminals a and b.
16
Chapter 6 EGR 271 – Circuit Theory I

## Slide 17
Leakage Resistance
If an ideal capacitor is “charged” to a certain voltage and is then open-circuited, it should maintain its voltage (and stored energy) forever. Actual capacitors will lose their voltage over time (some in a few seconds and others may take several hours). This is due to a very small leakage current which flows through the dielectric. This effect is modeled by adding a leakage resistance in parallel with the capacitor as shown below.
Typical Values of Leakage Resistance
Ceramic capacitor - 1000 M
Mica capacitor - 1000 M
Polyester-film capacitor - 100 M
Electrolytic capacitor - 1 M
17
Chapter 6 EGR 271 – Circuit Theory I

## Slide 18
Stray Capacitance
We have seen that a capacitor can be formed using two parallel plates. This essentially means that any two surfaces could potentially act like a capacitor. This type of capacitance is referred to as stray capacitance.
Stray capacitance is usually very small (less than a few pF), but can cause serious problems at high frequency. For this reason, many high frequency circuits use shielded cables and components.
Examples: Illustrate stray capacitance between:
a) two wires
b) the junctions in an npn BJT (transistor)
18
Chapter 6 EGR 271 – Circuit Theory I

## Slide 19
Two key facts about capacitors:
1) A capacitor’s voltage cannot change instantaneously.
  This is sometimes expressed as VC(0+) = VC(0-)
  Discussion:
2) A capacitor looks like an open-circuit in steady-state.
  “Steady-state” means that there have been no recent changes in the circuit or that any changing voltages or currents have had time to reach their final values.
  Discussion:
19
Chapter 6 EGR 271 – Circuit Theory I

## Slide 20
Example: In the circuit shown below the capacitors are initially uncharged. The switch closes at t = 0 and after a “long time” the circuit reaches steady-state. Find the voltage across each capacitor after the circuit reaches steady-state.
t = 0
20
Chapter 6 EGR 271 – Circuit Theory I

## Slide 21
Example: The switch had been closed for a long time before it was opened at t = 0.
21
Chapter 6 EGR 271 – Circuit Theory I

## Slide 22
Inductors
An inductor is a passive device created by wrapping wire around a core. When time-varying current passes through the coil a magnetic field is created and a voltage is “induced” across the coil. Inductors are also called “chokes” or “coils”.
f
core
magnetic
field lines
windings (N = 5.5 turns in this diagram)
magnetic flux, f
i(t)
+ v(t) -
A current, i(t) is passed through the windings
A voltage, v(t) is “induced” across the windings
22
Chapter 6 EGR 271 – Circuit Theory I

## Slide 23
Magnetic flux
In the previous diagram it was shown that a magnetic flux, , flowed through the core.
Magnetic flux is measured in units of Webers, Wb. It is somewhat like a magnetic current flowing through the core. The direction of the magnetic flux is determined using the “right-hand rule”.
Right-hand rule: Using your right hand, curl your fingers in the direction that the current flows through the coil and your thumb will indicate the direction of the magnetic flux.
Example: Sketch inductors with various types of cores and show the magnetic flux.
23
Chapter 6 EGR 271 – Circuit Theory I

## Slide 24
Inductance
N = number of windings around the core
 = flux linkage = N
 is also proportional to the current or  = (constant)i
This constant is referred to as inductance, L
 = N = Li
So a key relationship for inductors is:
The voltage induced across the coil is equal to the derivative of the flux linkage, so
Notes:
1) This equation is sort of like “Ohm’s Law” for an inductor.
2) Be sure to use passive sign convention
3) Note that the inductor symbol looks like a coil of wire.
Note: More detailed information on magnetic fields is covered in a later course in electromagnetics.
24
Chapter 6 EGR 271 – Circuit Theory I

## Slide 25
Physical Characteristics
The value of L can also be determined from the physical properties of the inductor using
Where N = number of turns
A = cross-sectional area of the core (in m2)
lc = length of the core (in m)
 = permeability of the core
A = cross-sectional
area of the core (in m2)
lC = length of core (in m)
N = number of turns (complete 360 wraps)
25
Chapter 6 EGR 271 – Circuit Theory I

## Slide 26
Permeability of the core
Permeability can be thought of as a measure of how well a type of material can sustain a magnetic field.
 = permeability of the core. This is typically expressed as:
 = Ro
where o = 4 x 10-7 Wb/Am and R = relative permeability
There are only basically two values for R :
R = 1 for non-ferrous materials
R  200 for ferrous materials
The equation for inductance can now be written as:
So the value of L is increased by a factor of 200 simply by using an iron core!
26
Chapter 6 EGR 271 – Circuit Theory I

## Slide 27
Typical values
Inductors are sometimes classified in two broad categories:
1) iron-core inductors - typical values in the H range
2) non-iron core inductors - typical values in the H or mH range
Demonstration - Pass around various types of inductors in class.
Example - Calculate the approximate value of L for one of the inductors in class by estimating the dimensions and the number of turns.
27
Chapter 6 EGR 271 – Circuit Theory I

## Slide 28
Examples of inductors (www.allelectronics.com)
220uH drum choke
Variable choke with adjustable ferrite
3.5mH bobbin choke
390uH choke coil
346uH inductor (toroid)
4mH high-current choke
28
Chapter 6 EGR 271 – Circuit Theory I

## Slide 29
Examples of inductors (www.ctparts.com)
Air-core inductor
Peaking coils
Power inductor
Power line choke
Wire-wound inductors
Toroidal power chokes
(www.coilcraft.com)
29
Chapter 6 EGR 271 – Circuit Theory I

## Slide 30
Key inductor relationships:
Show that
30
Chapter 6 EGR 271 – Circuit Theory I

## Slide 31
Example: Find i(t) through the inductor shown if v(t) = 2e-40t V. Assume that there is no initial energy stored in the inductor.
Example: The toroidal inductor shown has L = 46 mH and is rated for a maximum current of 2A. What is the maximum energy that could be stored in the inductor?
Example: Find v(t) across the inductor if i(t) = 10cos(400t) mA.
31
Chapter 6 EGR 271 – Circuit Theory I

## Slide 32
Example: Sketch v(t), p(t), and w(t) if the graph of i(t) shown below represents the current through a 2H inductor.
32
Chapter 6 EGR 271 – Circuit Theory I

## Slide 33
Series Inductance
KVL can be used to show that:
(Series inductors combine like series resistors)
Example: Find the equivalent inductance between terminals a and b.
Parallel Inductance
KCL can be used to show that:
(Parallel inductors combine like parallel resistors)
33
Chapter 6 EGR 271 – Circuit Theory I

## Slide 34
Non-ideal effects in inductors
Resistors and capacitors typically act quite closely to their ideal models. Inductors, however, often do not. There are numerous non-ideal effects in inductors, including:
  coil resistance
  eddy currents
  hysteresis
  L varies somewhat with current (it should be a constant)
  L varies somewhat with frequency (it should be constant)
Additionally, inductors are often bulky compared to capacitors. In some cases, circuits with capacitors or inductors can be used to perform the same function. In these cases, capacitor circuits are preferred due to the problems with inductors listed above.
Inductor models often include a series coil resistance, as shown below.
Typical values of Rcoil:
From a few ohms (small inductors) to hundreds of ohms (large iron-core inductors).
34
Chapter 6 EGR 271 – Circuit Theory I

## Slide 35
Two key facts about inductors:
1) An inductor’s current cannot change instantaneously.
  This is sometimes expressed as IL(0+) = IL(0-)
  Discussion:
2) An inductor looks like a short-circuit in steady-state.
  “Steady-state” means that there have been no recent changes in the circuit or that any changing voltages or currents have had time to reach their final values.
  Discussion:
35
Chapter 6 EGR 271 – Circuit Theory I

## Slide 36
Example: The inductors in the circuit shown below have no initial stored energy. The switch closes at t = 0 and after a “long time” the circuit reaches steady-state. Find the current through each inductor after the circuit reaches steady-state.
36
Chapter 6 EGR 271 – Circuit Theory I

## Slide 37
Example: The circuit below was in steady state before the switch opened at t = 0. Find i(0-), i(0+), v(0-), v(0+), and di(0+)/dt.
+
_
18 V
t = 0
3
3
2H
v(t)
+
_
i(t)
6
37
Chapter 6 EGR 271 – Circuit Theory I

## Slide 38
Example: Find v(t) in the circuit below if i(t) = 10e-4t A. Assume that there is no initial stored energy in the circuit.
38
Chapter 6 EGR 271 – Circuit Theory I