## Slide 1
MATLAB Lecture #1 EGR 271 – Circuit Theory I
MATLAB in EGR 271-272
MATLAB is a powerful and widely used application for mathematics and engineering. It is commonly used by electrical and computer engineers and it is highly likely that electrical and computer engineering students will use MATLAB in later courses and as working engineers.
MATLAB will be used in EGR 271-272 in many areas, including:
Solving systems of equations
Performing symbolic calculations
Writing interactive programs
Determining graphical results
Analyzing AC circuits using complex numbers
Analyzing circuits and systems using with Laplace transforms

## Slide 2
MATLAB Student Edition
We will use MATLAB routinely in this course. Although MATLAB is available on campus in H-151, H-164, and H-208, it would be advantageous to purchase a copy of the student edition of MATLAB. The student version is full-featured and will be useful in later courses as well. To purchase the student edition, do a quick online search for “MATLAB student edition” or go to: http://www.mathworks.com/academia/student_version/
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 3
MATLAB Student Edition
If you purchase the student edition of MATLAB you will need to set up a new account using your TCC email address. Note that there are additional add-on products available with MATLAB, but we will only need the standard student version as indicated below.
Check this box only
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 4
MATLAB Basics (mostly review from EGR 110)
MATLAB is typically covered in EGR 110, so it is assumed that most students have a basic understanding of MATLAB. Any students that are not familiar with MATLAB may need to spend more time reviewing this presentation or the presentations from EGR 110.
MATLAB presentations from EGR 110 are available at: http://faculty.tcc.edu/pgordy/EGR110/index.htm
The instructor may go through the slides in this presentation very quickly or simply skip to the end and demonstrate MATLAB using some of the examples at the end of the presentation. You can refer to this presentation as you work on assignments.
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 5
MATLAB Environment
When MATLAB is launched, several windows will appear. An important part of learning MATLAB is learning how to use each of these windows.
As we will see later, MATLAB uses a number of
other windows as well, including:
Editor – for creating and editing MATLAB programs
Array editor
Help window
Properties windows
Command Window
Current Folder Window
Command History Window
Workspace Window
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 6
Vectors and scalars in MATLAB
MATLAB is designed to work with vector quantities or matrices, where the elements of the vector or matrix are placed inside brackets [ ] with the elements in each row separated by spaces and the rows separated by semicolons. However, MATLAB can also be used to work with variables defined by a single value called scalars.
Example:
Type of quantity Mathematical notation: MATLAB notation:
Vector A = [2 3 4;7 9 –1]
Scalar x = 2 x = 2
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 7
Variable names in MATLAB
are case-sensitive
can contain up to 63 characters (any characters beyond the 63rd are ignored)
must start with a letter, followed by any comb. of letters, numbers, and underscores
cannot contain spaces
Exercise: Indicate whether each variable used below is valid or invalid.
Inductive Reactance = 12.5; Valid/Invalid
2nd _derivative = 10; Valid/Invalid
X1X2X3 = 54; Valid/Invalid
Energy-Delivered = 1.25E6; Valid/Invalid
Fifteen = 16; Valid/Invalid
Problem_5.2_Answer = 7; Valid/Invalid
Capacitor_Voltage = 125; Valid/Invalid
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 8
Expressions in MATLAB
MATLAB, like most programming languages, requires that expressions contain a single variable to the left of the assignment operator (equals sign).
Example:
X = 2*A + 3*B - 15
Single
variable
Assignment
operator
Expression involving variables, functions, numbers, etc
Additionally, MATLAB performs the calculations to the right of the assignment operator (=) using existing values of variables and then assigns the result to the variable to the left of the equals sign.
So the expression X = X + 2 should be interpreted as Xnew = Xold + 2
Note the result of the following sequence of instructions in MATLAB (try it!):
Note: a semicolon (;) after a command suppresses the value from being printed
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 9
MATLAB’s Basic Scalar Arithmetic Operators
Operation
Symbol
Example
Addition
+
X = A + B
Subtraction
-
X = A - B
Multiplication
*
X = A*B
Division
/
X = A/B
Exponentiation
^
X = A^2 + B^2
Operation
Symbol
Precedence
Parentheses
( )
Highest
Exponentiation
^
Negation
-
Multiplication or division
* or /
Addition or subtraction
+ or -
Lowest
MATLAB’s Order of Operations (for scalars)
Operators are executed left to right using the following precedence.
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 10
Function
Description
pi
returns  to 15 significant digits
cos(x)
returns cosine of x, with x in radians
sin(x)
returns sine of x, with x in radians
tan(x)
returns tangent of x, with x in radians
acos(x)
returns arccosine of x, in radians
asin(x)
returns arcsine of x, in radians
atan(x)
returns arctangent of x, in radians
exp(x)
returns the value of ex
sqrt(x)
returns the square root of x
factorial(x)
returns factorial of x
log(x)
returns ln(x)
log10(x)
returns log10(x)
abs(x)
returns absolute value of x
sinh(x)
returns the hyperbolic sine of x
round(x)
rounds x off toward nearest integer
ceil(x)
rounds x toward positive infinity
floor(x)
rounds x toward negative infinity
MATLAB built-in functions
MATLAB has hundreds of built-in functions. A few of the functions commonly used with scalars are shown in the table.
More functions
Open MATLAB and select Help – Function Browser and check out the vast number of functions available in MATLAB. What do the following functions do?
sind(A)
hypot (a,b)
cot(A)
mod(N,M)
atan2(y,x)
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 11
MATLAB Command
Description
Example
X = 2/3 displayed as:
format short
express using 4 digits after decimal point (default)
0.6667
format long
express using 14 digits after decimal point (d.p.)
0.66666666666667
format rat
express using a ratio of two integers
2/3
format bank
express using 2 digits after d.p.
0.67
format short e
express in scientific notation w/ 4 digits after d.p.
6.6667e-001
format long e
express in scientific notation w/ 14 digits after d.p.
6.666666666666667e-001
format compact
suppresses blank lines in the output (Nice option!)
(see example below)
MATLAB Format Commands
MATLAB offers a few commands for controlling the format of the output. Additional useful commands are provided on the next page.
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 12
MATLAB Command
Description
clc
clear the Command Window
clear
clear values of all variables
disp(x)
display value of a single variable or expression
(see examples below)
fprintf(a,b,c,…)
Display values of variables and text with a desired number of digits (see examples on the next page).
Formatting can include:
‘\n’ – linefeed (carriage return)
‘\t’ – tab
‘%0.4f’ – use fixed format w/4 digits after the decimal point (dp)
‘%9.4f – use fixed format w/4 digits after the dp and 9 total spaces
‘%0.4e’ – use scientific notation w/4 digits after dp
‘%0.4g’ – use 4 significant digits (in fixed or scientific)
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 13
Example using fprintf( )
Text
MATLAB Lecture #1 EGR 271 – Circuit Theory I
% - start of formatter
0 - use as many spaces as needed
2 - use 2 digits after dp
f - use a fixed (f) format (i.e., not scientific notation)
Text
\n = “newline” character (go to a new line)
Variable to be printed with the formatter
Output:

## Slide 14
Additional examples using fprintf( )
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Output:
12 spaces

## Slide 15
MATLAB Script Files (.m files)
We have seen how to execute MATLAB commands in the Command Window. We will now see how to write a program in MATLAB. The program (called a script file or .m file) is a file containing a series of statements much like those used previously in the Command Window. A program has the advantage of being reusable. You can easily try a sequence of commands and then modify them if the output isn’t correct. The program can be executed by typing its name in the Command Window.
The Current Directory
When the name of a program is entered into the Command Window, MATLAB looks for the program in the Current Directory and executes it if it is located there.
Run program example.m in the current folder
The Current Folder is shown here.
MATLAB
files in current folder
Change current folder here
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 16
Changing the Current Folder
It is recommended that you change the current folder to the folder on your personal drive where you will save your files.
Add a New Folder
Current Folder has been changed
Change drive and folders
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 17
Creating a script (.m) file
Type edit in the Command Window to run the MATLAB editor
MATLAB editor
Notes:
Type edit to open the editor
Type edit MyFile.m to create a new file named MyFile.m (if it does not exits)
Type edit MyFile.m to open an existing file named MyFile.m
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 18
Using MATLAB’s INPUT function
The following MATLAB function is used to prompt the user to enter inputs:
input (‘message’) % returns a value entered from the keyboard.
Example:
R = input(‘Enter the resistance in ohms’);
Example:
Write a MATLAB program to calculate the power absorbed by a resistor.
Prompt the user to enter the resistance and the voltage.
Display the input values and the output (with units).
Solution – next page
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 19
Sample MATLAB program
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Sample Output:
Run the program by selecting Run in the editor or by entering Resistor_Power in the Command Window.

## Slide 20
Symbolic Expressions in MATLAB
MATLAB is a powerful tool for working with symbolic expressions.
Useful operations with symbolic expressions include:
Solving for variables as functions of other variables (algebraic manipulation)
Solving simultaneous equations
Finding derivatives and integrals
Solving differential equations (useful in EGR 272)
Finding Laplace and inverse Laplace transforms (useful in EGR 272)
Much more!
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Output:

## Slide 21
Example:
Use MATLAB to find a symbolic solution to the quadratic equation.
Use the symbolic function solve( ).
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 22
Example: - Some modifications to the previous example:
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Output:
Output:

## Slide 23
Symbolic versus numeric result
Note that there is often no difference between solving equations that have a numeric result and equations that have a symbolic result. It is simply a matter of the number of equations versus the number of unknowns.
Example: 2 equations, 2 unknowns  numeric solution
Example: 2 equations, 3 unknowns  symbolic solution
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 24
Example – solving simultaneous equations:
Use MATLAB to solve the following two simultaneous equations (with numeric results): 2x + 3y = 14
x - y = -3
Use the symbolic function solve( ).
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Note: We will introduce simpler methods for solving simultaneous equations with numeric results later.

## Slide 25
Symbolic substitution:
If we would like to evaluate a symbolic expression for specific values, we can use the symbolic substitution function in MATLAB: subs( )
Example: If V1 = 10e-10t, find symbolic expressions for V1 and
P1 = (V1)2/R1. Then use subs( ) to find numeric values for V1 and P1 when t = 50 ms and R1 = 20 ohms.
MATLAB Lecture #1 EGR 271 – Circuit Theory I
V1 = 6.0653 V when t = 50 ms
P1 = 1.8394 W when t = 50 ms and R1 = 20 ohms

## Slide 26
Finding derivatives in MATLAB
diff(f ) – finds the derivative of symbolic function f
diff(f, 2) – finds the 2nd derivative of f
(same as diff(diff(f))
If f is a function of both x and y,
diff(f, x) – partial derivative of f w.r.t. x
diff(f, y) – partial derivative of f w.r.t. y
Examples: (shown to the right)
Before proceeding with more advanced derivatives and applications, it may be useful to discuss different ways of representing functions in MATLAB.
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 27
Performing integration in MATLAB
int(S) – finds the indefinite integral of a symbolic expression S with respect to its symbolic variable (or variable closest to x)
int(S, z) – finds the indefinite integral of a symbolic expression S with respect to z
int(S, a, b) – finds the definite integral of a symbolic expression S from a to b with respect to its symbolic variable (or variable closest to x)
int(S, z, a, b) – finds the definite integral of a symbolic expression S from a to b with respect to z
double(int(S, z, a, b)) – finds a numeric result for the definite integral of a symbolic expression S from a to b with respect to z. This is useful in cases where MATLAB can’t find a symbolic solution.
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 28
MATLAB Examples:
MATLAB Lecture #1 EGR 271 – Circuit Theory I

## Slide 29
Writing a program requiring inputs and formatted output:
  Write MATLAB program to do the following:
  Prompt the user to enter the value of R1 in ohms
  Prompt the user to enter the value of R2 in ohms
  Calculate R1 || R2 and display the result in ohms (with 1 digit after the decimal point).
  If you enter R1 = 20 and R2 = 30, try to format the output to look as follows:
    R1 = 20.0 ohms, R2 = 30.0 ohms, Result: 12.0 ohms
    R1 = 20.0 ohms
    R2 = 30.0 ohms
    R1 || R2 = 12.0 ohms
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Classroom Demonstration: Try the following examples on your own or the instructor may demonstrate them in class.
Command Window: Try some simple calculations using the command window.
  Calculate V and P if R = 1.2 k and I = 3.75 mA
  Try using clc, format compact, and clear
  Try using format long, format rat, and format short
  Try editing expressions already executed using the Command History window or using the up and down arrows.

## Slide 30
Calculus:
  If Q1 = 10e-4t mC, use MATLAB to find a symbolic expression for I1
  If V2 = 10e-1000t V and I2 = 20e-2000t mA:
    Find a symbolic expression for P2 = V2*I2
    Evaluate P2 at time t = 1ms
    Find a symbolic expression for W2
    Find the energy from 0 to 1ms
MATLAB Lecture #1 EGR 271 – Circuit Theory I
Classroom Demonstration: Try the following examples on your own or the instructor may demonstrate them in class.
Symbolic manipulation: Solve for IX in the following symbolic expression (KVL in a simple series circuit): -V + IX*R1 + IX*R2 + IX *R3 = 0
(Note that Ix was used instead of I. Avoid using variables i, j, or I in MATLAB.)