## Slide 1
Read: Chapter 9 and Appendix B in Electric Circuits, 10th Edition by Nilsson
Sinusoidal Steady-State Analysis
also called AC Circuit Analysis
also called Phasor Analysis
Discuss each name.
Before beginning a study of AC circuit analysis, it is helpful to introduce (or review) two related topics:
1) sinusoidal waveforms
2) complex numbers
1
Chapter 9 EGR 272 – Circuit Theory II

## Slide 2
Sinusoidal Waveforms
In general, a sinusoidal voltage waveform can be expressed as:
v(t) = Vpcos(wt) where
Vp = peak or maximum voltage
w = radian frequency (in rad/s)
T = period (in seconds)
f = frequency in Hertz (Hz)
Example: An AC wall outlet has VRMS = 120V and f = 60 Hz. Express the voltage as a time function and sketch the voltage waveform.
2
Chapter 9 EGR 272 – Circuit Theory II

## Slide 3
Shifted waveforms:
v(t) = Vpcos(wt +  ) where  = phase angle in degrees
a shift to the left is positive and a shift to the right is negative (as with any function)
Example: Sketch v(t) = 50cos(500t – 30o)
Radians versus degrees:
Note that the argument of the cosine in v(t) = Vpcos(wt +  ) has mixed units – both radians and degrees. If this function is evaluated at a particular time t, care must be taken such that the units agree.
Example: Evaluate v(t) = 50cos(500t – 40o) at t = 1ms.
3
Chapter 9 EGR 272 – Circuit Theory II

## Slide 4
Relative shift between waveforms:
Example: v1(t) = 50cos(500t – 50o) and v2(t) = 40cos(500t + 60o).
Does v1 lead or lag v2? By how much?
If v1 was shifted 0.5ms to the right, find a new expression for v1(t).
4
Chapter 9 EGR 272 – Circuit Theory II
V1 leads V2 by 
or
V2 lags V1 by 

## Slide 5
Complex Numbers
A complex number can be expressed in two forms:
Rectangular form
Polar form
A complex number can be plotted on the complex plane, where
x-axis: real part of the complex number
y-axis: imaginary (j) part of the complex number
5
Chapter 9 EGR 272 – Circuit Theory II

## Slide 6
Rectangular Numbers
A rectangular number specifies the x,y location of complex number in the complex plane in the form:
6
Chapter 9 EGR 272 – Circuit Theory II
(rectangular form)

## Slide 7
Polar Numbers
A polar number specifies the distance and angle of complex number from the origin in the complex plane in the form:
7
Chapter 9 EGR 272 – Circuit Theory II

## Slide 8
Converting between rectangular form and polar form
  Polar to Rectangular: Rectangular to Polar:
  Given: |X|,  Given: A, B
  Find: A, B Find: |X|, 
A = |X|cos()
B = |X|sin()
8
Chapter 9 EGR 272 – Circuit Theory II

## Slide 9
Mathematical Operations Using Complex Numbers
Note: Calculators are used for most numerical calculations. When symbolic calculations are used, the following items may be helpful.
1) Addition/Subtraction – easiest in rectangular form
9
Chapter 9 EGR 272 – Circuit Theory II
Complex numbers using calculators
Refer to the handout entitled “Complex Numbers”

## Slide 10
2) Multiplication/Division – easiest in polar form
3) Inversion
10
Chapter 9 EGR 272 – Circuit Theory II

## Slide 11
4) Exponentiation
5) Conjugate
Example:
11
Chapter 9 EGR 272 – Circuit Theory II

## Slide 12
Example: Convert to the other form or simplify.
1) -3 2) -j3
3) j6 4) -4/j
5) 1/(j2) 6) j2
7) j3 8) j4
9) 300 – j250 10) 250-75°
11) (-3 - j6)* 12) (250-75°)*
13) (4 + j7)2 14) (-4 + j6)-1
12
Chapter 9 EGR 272 – Circuit Theory II

## Slide 13
Example: Simplify the following (by hand or using a calculator)
13
Chapter 9 EGR 272 – Circuit Theory II
Note for Mastering Engineering:
If a problem asks you to enter a result as a “complex number”, use rectangular form.
If a problem asks you to enter a result in “polar form”, use polar form.

## Slide 14
Phasor Analysis
The use of complex numbers to solve ac circuit problems – the so-called phasor method considered in this chapter – was first done by German-Austrian mathematician and electrical engineer Charles Proteus Steinmetz in a paper presented in 1893. He is noted also for the laws of hysteresis and for his work in manufactured lighting.
Steinmetz was born in Breslau, Germany, the son of a government railway worker. He was deformed from birth and lost his mother when he was 1 year old, but this did not keep him from becoming a scientific genius. Just as his work on hysteresis later attracted the attention of the scientific community, his political activities while he was at the University at Breslau attracted the police. He was forced to flee the country just as he had finished the work for his doctorate, which he never received. He did electrical research in the United States, primarily with the General Electric Company. His paper on complex numbers revolutionized the analysis of ac circuits, although it was said at the time that no one but Steinmetz understood the method. In 1897 he also published the first book to reduce ac calculations to a science.
(Electric Circuit Analysis, 2nd Edition, by Johnson, Johnson, and Hilburn, p. 307)
“I have found the equation that will enable us to transmit electricity through alternating current over thousands of miles. I have reduced it to a simple problem in algebra.”
Charles Proteus Steinmetz
14
Chapter 9 EGR 272 – Circuit Theory II

## Slide 15
Examples: Convert to the other notation (time waveform or phasor)
Phasor – a complex number in polar form representing either a sinusoidal voltage or a sinusoidal current.
Symbolically, if a time waveform is designated at v(t), then the corresponding phasor is designated by .
15
Chapter 9 EGR 272 – Circuit Theory II
Should phasors use cos( ) or sin( )?
It doesn’t matter as long as you are consistent.
Our textbook typically uses cos( ).

## Slide 16
Justification for “phasor analysis” Consider the circuit shown below.
v1(t) and v2(t) must have the same form as the voltage source, v(t) (or forcing function).
So v1(t) = V1cos(wt+) and v2(t) = V2cos(wt+)
KVL yields: v(t) = v1(t) + v2(t) (KVL in the time-domain)
VPcos(wt+) = V1cos(wt+) + V2cos(wt+)
Now replacing the equation by an equation with the same real part:
VPej(wt+) = V1ej(wt+) + V2ej(wt+)
Dividing by ejwt yields
VPej  = V1ej + V2ej
But these are simply polar numbers (in true polar form) so
VP  = V1  + V2  or
(KVL using phasors)
16
Chapter 9 EGR 272 – Circuit Theory II
This is essentially a short proof showing why phasor analysis works.

## Slide 17
Note that the relationship above is similar to Ohm’s Law.
Now we will define impedance for resistors, inductors, and capacitors.
Resistors:
If i(t) = Ipcos(wt + ), find v(t) and show that
Before we get into the details of phasor analysis, we need a method of representing components in AC circuits. We will introduce a new term called impedance.
Complex Impedance
Z = impedance or complex impedance (in )
17
Chapter 9 EGR 272 – Circuit Theory II

## Slide 18
Inductors:
If i(t) = Ipcos(wt + ), find v(t) and show that
Capacitors:
If v(t) = Vpcos(wt + ), find i(t) and show that
18
Chapter 9 EGR 272 – Circuit Theory II

## Slide 19
Example: Find I(t) in the circuit below using phasor analysis.
19
Chapter 9 EGR 272 – Circuit Theory II
AC Circuit Analysis Procedure:
1) Draw the phasor circuit (showing voltage and current sources as phasors and using complex impedances for the components).
2) Analyze the circuit in the same way that you might analyze a DC circuit.
3) Convert the final phasor result back to the time domain.

## Slide 20
KVL and KCL in AC circuits:
KVL and KCL are satisfied in AC circuits using phasor voltages and currents. They are not satisfied using the magnitudes of the voltages or the currents.
Example: For the previous example, show that:
20
Chapter 9 EGR 272 – Circuit Theory II
Example: For the previous example, show that
using a phasor diagram.

## Slide 21
Example: Analyze the circuit below using phasor analysis. Specifically,
A) Find the total circuit impedance
B) Find the total current, i(t) (Example is continued on the following slide)
21
Chapter 9 EGR 272 – Circuit Theory II

## Slide 22
Example: (continued)
C) Use current division to find i1(t) and i2(t)
Show that KCL is satisfied using current phasors, but not current magnitudes.
E) Show that KCL is satisfied using a phasor diagram.
22
Chapter 9 EGR 272 – Circuit Theory II

## Slide 23
Using Phasors to Add Sinusoids
Sinusoidal voltages or currents could be added using various trigonometric identities; however, they are more easily combined using phasors.
Example: If v1 = 10cos(200t + 15), v2 = 15cos(200t + -30), and v3 = 8sin(200t), find v4.
V1
+
_
V3
+
_
V2
+
_
V4
+
_
23
Chapter 9 EGR 272 – Circuit Theory II

## Slide 24
Review of DC Circuit Analysis Techniques
Analyzing AC circuits is very similar to analyzing DC resistive circuits. Several examples are presented below which will also serve to review many DC analysis techniques, including:
Source transformations
Mesh equations
Node equations
Superposition
Operational Amplifiers (op amps)
Thevenin’s and Norton’s theorems
Maximum Power Transfer theorem
24
Chapter 9 EGR 272 – Circuit Theory II

## Slide 25
Source transformations
A phasor voltage source with a series impedance may be transformed into a phasor current source with a parallel impedance as illustrated below. The two sources are identical as far as the load is concerned.
Notes:
Not all sources can be transformed. Discuss.
The two sources are not equivalent internally. For example, the voltage across Zs is not equivalent to the voltage across Zp.
Dependent sources can be transformed.
Converting a real current source
to a real voltage source:
Converting a real voltage source
to a real current source:
25
Chapter 9 EGR 272 – Circuit Theory II

## Slide 26
Example: Solve for the voltage V using source transformations.
26
Chapter 9 EGR 272 – Circuit Theory II

## Slide 27
Mesh equations:
Example: Solve for the voltage V using mesh equations.
27
Chapter 9 EGR 272 – Circuit Theory II

## Slide 28
Node equations:
Example: Solve for the current i(t) using node equations.
28
Chapter 9 EGR 272 – Circuit Theory II

## Slide 29
Superposition:
Superposition can be used to analyze multiple-source AC circuits in a manner very similar to analyzing DC circuits. However, there are two special cases where it is highly recommended that superposition be used:
Circuits that include sources at two or more different frequencies.
Circuits that include both DC and AC sources (Note: you could think of DC
sources as acting like AC sources with w = 0.)
Example 1 (sources with different frequencies): Solve for the voltage V using superposition.
29
Chapter 9 EGR 272 – Circuit Theory II

## Slide 30
Example 2 (AC and DC sources): Solve for the voltage V using superposition.
30
Chapter 9 EGR 272 – Circuit Theory II

## Slide 31
Thevenin’s and Norton’s Theorems – Recall that any one-port network N may be represented by either of the following types of equivalent circuits:
Thevenin Equivalent Circuit (TEC) – consisting of a voltage source and a series impedance
Norton Equivalent Circuit (NEC) – consisting of a current source and a parallel impedance
31
Chapter 9 EGR 272 – Circuit Theory II
where:
Network N
independent sources, dependent sources, and resistors
Load
+
V
_
I
+
-
RTH
VTH
Load
+
V
_
I
RN
IN
TEC
NEC
Load
+
V
_
I
Network N (independent sources,
dependent sources,
and resistors)

## Slide 32
32
Chapter 9 EGR 272 – Circuit Theory II
Thevenin’s and Norton’s Theorems with AC Circuits:
Thevenin’s and Norton’s theorems apply to AC circuits as well, but
and are now phasors and RTH or RN are replaced by ZTH or ZN as shown below.
Network N
independent sources, dependent sources, and resistors
Load
+
V
_
I
Network N (independent sources,
dependent sources,
resistors, capacitors, & inductors)
Load
+
V
_
I
+
-
ZTH
VTH
TEC
Load
+
V
_
I
ZN
IN
NEC
where:

## Slide 33
33
Chapter 9 EGR 272 – Circuit Theory II
Thevenin’s Theorem:
Example: Find the Thevenin Equivalent Circuit seen by RL in the circuit below.
+
_
50cos(5000t) V
30
3mH
5F
RL

## Slide 34
Op Amps - Analyzing op amps with AC sources is similar to analyzing op amps with other sources. Recall three key steps:
V+ = V- (the voltage is the same at the two input terminals)
I+ = I- = 0 (no current enters the op amp at the inputs)
Use node equations
Example: Solve for Vo and Io in the op am circuit below.
34
Chapter 9 EGR 272 – Circuit Theory II
Io
+
Vo
_
20cos(10t) V

## Slide 35
Impedance, Resistance, and Reactance
Recall that impedance, Z, is defined as follows:
Expressing Z in rectangular and polar form yields:
where:
and
Also note that
35
Chapter 9 EGR 272 – Circuit Theory II

## Slide 36
Impedance Diagram:
The relationship between Z, R, and X is sometimes illustrated using an impedance diagram as shown:
Re
Im
R
X
Z
|Z|

R
jX
|Z|

or
Inductive reactance:
Recall that the impedance for an inductor was defined as:
So inductive reactance is defined as follows:
or
36
Chapter 9 EGR 272 – Circuit Theory II

## Slide 37
Capacitive reactance:
Recall that the impedance for a capacitor was defined as:
So capacitive reactance is defined as follows:
or
Example:
If w = 100 rad/s, find:
The resistance of the circuit
The reactance of the circuit
If the impedance is to be represented by a series RC circuit, find R and C
If the impedance is to be represented by a parallel RC circuit, find R and C
V
I
+
_
37
Chapter 9 EGR 272 – Circuit Theory II

## Slide 38
Admittance, Conductance, and Susceptance
Admittance is defined as follows:
Expressing Y in rectangular form yields:
where:
()
Note that G and B can be expressed in terms of R and X as follows:
so
38
Chapter 9 EGR 272 – Circuit Theory II

## Slide 39
V
I
+
_
10uF
1.5k
Example:
If w = 10 rad/s for the circuit shown, find Z, |Z|, R, X, Y, G, and B
39
Chapter 9 EGR 272 – Circuit Theory II

## Slide 40
Resonance – the condition where the reactive components in a circuit cancel resulting in a purely resistive circuit. This condition can sometimes yield unusually large voltages or currents.
Series resonant circuit:
40
Chapter 9 EGR 272 – Circuit Theory II
Show that
+
_
Zeq
Vmcos(wt) V
R
L
C
i(t)

## Slide 41
Series Resonant Circuit: (continued)
Solve for the current and all component voltages both as phasors and functions of time. Sketch the time waveforms.
41
Chapter 9 EGR 272 – Circuit Theory II

## Slide 42
Series Resonant Circuit: (continued)
Define Qs = “Quality factor” for a series resonant circuit.
Show that
42
Chapter 9 EGR 272 – Circuit Theory II

## Slide 43
Example: The series RLC circuit below is in resonance.
43
Chapter 9 EGR 272 – Circuit Theory II
A) Determine the resonant frequency, wo (in rad/s) and fo (in Hz).
Draw the phasor circuit if w = wo. Label
Find
Sketch a phasor diagram illustrating the relationship between the voltages in the circuit.
+
_
100cos(wt) V
4
10mH
1uF
i(t)

## Slide 44
Parallel resonant circuit:
Also determine expressions for resistor, capacitor, and inductor current.
44
Chapter 9 EGR 272 – Circuit Theory II
+
V
_
Zeq
Imcos(wt) A
R
L
C
Show that

## Slide 45
Resonance in other circuits
The relationships developed for wo for series and parallel RLC circuits do not apply to other resonant circuits. The value of wo can be determined for other circuits by finding the total circuit impedance and determining at what frequency the total circuit impedance is real.
45
Chapter 9 EGR 272 – Circuit Theory II
Example: Find the resonant frequency, wo, for the circuit below. Compare it to the following incorrect formula:
+
_
Vmcos(wt) V
10
5H
0.1F

## Slide 46
Transformers:
Our earlier study of inductors introduced the idea that current through a set of windings creates a magnetic field and magnetic flux, , flows through the core. If  then flows through a second set of windings another magnetic field is created and a secondary voltage is induced across these windings. This arrangement of two windings on a common core is called a transformer (illustrated below).
46
Chapter 9 EGR 272 – Circuit Theory II

## Slide 47
Recall that
 = flux linkage
N = number of turns
 = magnetic flux (in Webers, Wb)
and  = N = Li , where L = inductance in Henries, H
Since the same magnetic flux, , flows through the windings it is also true that the rate of change of magnetic flux, d/dt is the same, so
Also
So
where a = turns ratio
47
Chapter 9 EGR 272 – Circuit Theory II

## Slide 48
so
Key transformer relationships
We just saw that
Similarly
where a = turns ratio
48
Chapter 9 EGR 272 – Circuit Theory II

## Slide 49
Transformer symbols
General Transformer
Iron-core Transformer
49
Chapter 9 EGR 272 – Circuit Theory II

## Slide 50
Examples of transformers (reference: www.allelectronics.com)
Primary: 120V
Secondary: 28V, 1.5A
Primary: 120V
Secondary: 40VCT, 0.25A
Primary: 110V
Secondary: 15V, 0.4A
Utility pole transformer
50
Chapter 9 EGR 272 – Circuit Theory II

## Slide 51
Examples of transformers (reference: www.allelectronics.com)
PC Mount Transformer
Primary: 120V
Secondary: 16VCT, 0.8A or 8V, 1.6A
Toroidal Transformer
Primary: 120V
Secondary: 8.5V and 9.4V
Up/Down Transformer
(110V to 220V) or (220V to 110V)
Variac (Variable Transformer)
Input: 110V
Output: 0 to 130V
51
Chapter 9 EGR 272 – Circuit Theory II

## Slide 52
Dot Convention
The direction of the windings in the secondary with respect to the direction of the windings in the primary determines the polarity of the secondary voltage. However, rather than showing the direction of the windings, dots are often placed at one end of each winding. Then the following convention applies:
Dot convention: “A positive voltage at one dotted terminal will produce a positive voltage at the other dotted terminal.”
Note that the relationships
Imply that:
the positive terminals of V1 and V2 are at the dotted terminals
I1 enters the dotted terminal and I2 leaves the dotted terminal
These voltage polarities and
current directions are indicated
to the right.
i2
V1
+
_
i1
V2
+
_
N1:N2
a : 1
52
Chapter 9 EGR 272 – Circuit Theory II

## Slide 53
Four Common Transformer Uses
Change voltage levels
Change current levels
Change impedance levels (impedance matching)
Isolation (e.g., to isolate the secondary load from the ground in the primary)
Examples: Show simple examples of the four transformer uses listed above.
53
Chapter 9 EGR 272 – Circuit Theory II

## Slide 54
Example: Determine the V1 and i2 in the circuit below. Find these values by:
A) Using KVL equations around each loop
i2
V1
+
_
2
20 mH
+
_
50cos(10t)
5
20 mF
2:1
54
Chapter 9 EGR 272 – Circuit Theory II

## Slide 55
Example: Determine the V1 and i2 in the circuit below. Find these values by:
B) Reflecting the impedance of the secondary to the primary.
i2
V1
+
_
2
20 mH
+
_
50cos(10t)
5
20 mF
2:1
55
Chapter 9 EGR 272 – Circuit Theory II
Note: There are two similar homework problems on transformers in addition to Mastering Engineering problems. See the handout “Ch. 9 - Extra Homework Problems” on the course website or in Blackboard.

## Slide 56
Example: Determine the value of Zab below.
10
1:2
10
10
3:1
10
1:2
b
a
Zab
56
Chapter 9 EGR 272 – Circuit Theory II

## Slide 57
Example: Recall the example presented in EGR 271 where a transformer was used to insure that maximum power was delivered to a 4 ohm speaker from the output of an amplifier with an output resistance of 100 ohms.
57
Chapter 9 EGR 272 – Circuit Theory II
Audio
Amplifier
Ro = 100
4  speaker
Case 1: 4  speaker is connected directly to the 100  output. Terrible results occur due to mismatched impedances. Recall that we need Ro = RTh for max power. “Impedance matching” is important in many applications.
Audio
Amplifier
Ro = 100
4  speaker
a:1
R1
R2
Case 2: A transformer is used to match the impedances.
What value of a (turns ratio is necessary?
a = ________
What impedance R1 is seen by the amplifier?
R1 = ________
What impedance R2 is seen by the speaker?
R2 = ________

## Slide 58
Transformer Models:
Transformers considered in this course have been considered to be ideal. Although transformer behavior is often close to ideal, there are cases where non-ideal behavior might be examined. The figures to the left (reference: Electric Power & Machinery by Matsch) show models of a transformer used to approximate non-ideal behavior. The resistances, R1 and R2, represent the resistance of the windings and the inductive reactances, Xl1 and Xl2, represent leakage magnetic flux.
58
Chapter 9 EGR 272 – Circuit Theory II
(Just for reference)